# BSIM model Look-Up Table.
Gennadiy Serdyuk <gena@analograils.com>

## Introduction
[TBD]
## Approach Description
General idea is very simple – substitute piece of computations with look-up table, saving on CPU time. To implement that simplest case – rectangular grid with regular step is chosen.
Two things done:
a) charge calculation is switched off
b) piece of code , which computes Ids (vbs, vgs, vds)
## Implementation
Code changes in b3ld.c include:
  - declarations
  - initializations
  - preparation of loops, compute corner values of cells
  - store LUT
  - interpolation
Other parts related to initialization and additional parameters:
  b3.c, b3ask.c, b3mask.c, b3mpar.c, b3par.c, b3set.c,
  bsim3def.h
## Usage
To use, can add the following parameters to .model, it supports 9 new parameters:
vgsmin, vgsmax, vgsnum
vdsmin, vdsmax, vdsnum
vbsmin, vbsmax, vbsnum
that are correspondently minimum and maximum expected voltages and number of grid points between them. Defaults are: -5, +5 and 20.
Reasonable (from convergence point of view) values are:
vgsmin, vgsmax, vgsnum = -5 +5 50
vdsmin, vdsmax, vdsnum = -5 +5 50
vbsmin, vbsmax, vbsnum = -5 +5 10

If actual voltage will go out of vxxmin..vxxmax range, full BSIM calculation will be performed
Device support 1 new parameter:
lut_mode = 0 1 or 2 or 3 (4 not fully supported)

0 - full BSIM model
1 - BSIM model w/o change calculation
2 - LUT used
3 - LUT with precision monitoring (output is not elaborated)
## Testing
- Models
  Testing was performed with models and circuits published at
  http://www-device.eecs.berkeley.edu/~bsim3/circuits.html
- dc, different no of points
  Some dc comparison was made, results are satisfactory, but were not put here yet. Indeed – comprehensive test set has to be done
  - normal ambient temp
  - below zero (temp dependency)
  - negative bias values
  - p-mos – one example – normal ambient
  [all - TBD]
- tran
  ./test/tran
  one circuit from the same BSIM source (“comprt”) was simulated. Results different form original but very close to simulation made w/o charge.
  Original results are located at ./test/tran/orig
  Golden results are at ./test/tran/golden
- tran, many devices, profile
  - absolute time
  - relative time

## Open questions
- Step/ accuracy and table size
  It is possible to set step basing on required accuracy
- Orthogonal grid with varied step (accuracy-driven)
  It is possible to use variable step grid, basin on I-V curve curvature and required accuracy.
- Triangle/ tetrahedral grid
  It is possible to use tetrahedral grid – that could be geometrically elegant solution.
## Conclusion
implemented LUT speed up for BSIM3 model speeds it up 40%. It may be possible to reach 50% speedup.
Observations show that model calculation can take up to 50% of total simulation time. Thus, LUT usage can give 25% total speedup.
To achieve better figures more radical approaches has to be used.